## Slide 1: TSDuck
An extensible toolbox for MPEG transport streams
Version 3.29

## Slide 2: Topics
TSDuck overview
Transport stream processor
PSI/SI table manipulation using XML or JSON
Extending TSDuck
TSDuck as an MPEG/DVB C++ library
Using TSDuck from Java and Python

## Slide 3: TSDuck overview
Process ISO/IEC 13818-1 transport streams
Set of low-level utilities
  extensible through plugins
« Batch & Bash » oriented
  command-line only, no fancy GUI
  one utility or plugin = one elementary function
  can be combined in any order
Written in C++
  reusable and extensible code
  Java and Python bindings
Available on Linux, Windows and macOS

## Slide 4: What TSDuck is / is not
TSDuck is a general-purpose toolbox for digital TV engineers
 lab, demo, test, integration, debug, end-to-end testing 
TSDuck is not an off-the-shelf ready-to-use specialized application for production and operations

## Slide 5: Sample usages (1/2)
TS acquisition (IP, HTTP, HLS, SRT, RIST, DVB, ATSC, ISDB, ASI)
TS analysis
Transmodulation
Analysis, edition, injection of PSI/SI
  using and editing PSI/SI in XML or JSON format
Service manipulation
  extract, remove, rename, etc.
SCTE 35 splicing injection, extraction and monitoring
MPE injection and extraction (Multi-Protocol Encapsulation)

## Slide 6: Sample usages (2/2)
Route, merge, fork TS between applications
Test bed for CAS or STB
  injection of test cases
  DVB or ATIS Scrambling with DVB SimulCrypt support
Extraction of specific streams
  T2-MI (DVB-T2 Modulator Interface)
  PLP’s (Physical Layer Pipe)
  Teletext subtitles
Any combination of the above and more…

## Slide 7: Availability
Web site
  https://tsduck.io/
Open-source code
    https://github.com/tsduck/tsduck
BSD license
  liberal, no GPL-like contamination
  can be used in all applications

## Slide 8: Delivery
Installation
  pre-built binary installers for Windows and Linux
    Fedora, CentOS, Ubuntu, Debian, Raspbian
    user’s contribution: Arch Linux (AUR)
  through Homebrew on macOS
    user’s contribution: MacPorts
Documentation
  user’s guide
    PDF, 500+ pages of references and examples
  programmer’s guide
    doxygen-generated, online on tsduck.io
    for C++, Java and Python developers

## Slide 9: tsp
the transport stream processor

## Slide 10: tsp overview
Transport stream processing framework
  Combination of elementary processing using plugins
  One input plugin
    receive a TS from various sources
  Any number of packet processing plugins
    perform transformations on TS packets
    may remove packets
    may NOT add packets
  One output plugin
    send the resulting TS to various destinations

## Slide 11: tsp plugin chain

## Slide 12: tsp plugins
Each tsp plugin is a shareable library
  .so (Linux), .dylib (macOS), .dll (Windows)
  plus some embedded plugins, not seen as shareable libraries
File naming
  plugin named foo in file tsplugin_foo.so (or .dylib or .dll)
General command line syntax
  tsp [tsp-options] -I input-name [input-options] -P processor-name [processor-options]
  ... -O output-name [output-options]

## Slide 13: tsp basic syntax
TS acquisition
  tsp –I dvb –-uhf 21 -P until –-seconds 20 -O file capture.ts
Display the PMT of a selected service
  tsp –I dvb –-uhf 35 -P zap france2 -P sifilter –-pmt -P tables –-max 1 -O drop
capture DVB stream from UHF channel 21
save packets to file capture.ts
pass packets during 20 seconds, then stop
extract service « France 2 », rebuild SPTS
extract PID containing the PMT
display one table, then stop
drop output packets

## Slide 14: Simple examples
Transmodulation of a service over IP multicast
  tsp –I dvb –-uhf 35 -P zap france2 –-audio fra -O ip 224.10.11.12:1000
On-the-fly replacement of a PSI / SI table
  tsp -I dvb --uhf 24 -P inject nit.xml --pid 16 --replace –-stuffing -O dektec --uhf 24 --convolution 2/3 --guard 1/3
extract service « France 2 », keeping only one audio track
broadcast resulting SPTS to multicast IP address:port
replace content of PID 16 with table from an XML file (a NIT)
send modified TS to a Dektec modulator on same frequency

## Slide 15: Sample CAS test bed (1/2)
example using French DVB-T network:
duplicate and rename a TS, scramble one service

## Slide 16: Sample CAS test bed (2/2)
tsp -I dvb -u $UHF_INPUT
-P tsrename -t 9 -a
-P svrename direct8 -i 0x0901 -l 41 -n "Direct 8 Test"
-P svrename bfmtv -i 0x0903 -l 42 -n "BFM TV Test"
-P svrename 'i>tele' -i 0x0904 -l 43 -n "i>TELE Test"
-P svrename virgin17 -i 0x0905 -l 44 -n "Virgin 17 Test"
-P svrename gulli -i 0x0906 -l 45 -n "Gulli Test"
-P svrename france4 -i 0x0907 -l 46 -n "France 4 Test"
-P svrename 0x02FF -i 0x09FF
-P scrambler GulliTest -e $ECMG -s $SUPER_CAS_ID
-p $PMT_CADESC_PRIVATE -a $AC
-b $ECM_BITRATE --pid $ECM_PID
-P cat -c -a $CAS_ID/$EMM_PID/$CAT_CADESC_PRIVATE
-P datainject -r -s $MUX_SERVER_PORT
-b $EMM_MAX_BITRATE -p $EMM_PID
-O dektec -u $UHF_OUTPUT --convolution 2/3 --guard 1/32
rename the TS, rename all services in the TS
(service name, service id, LCN)
scramble one service, connect to a real ECM Generator, update PMT, insert ECM’s
accept connection from a real EMM Generator, update the CAT, insert EMM’s

## Slide 17: Sample MPE injection and extraction

## Slide 18: Multiple tsp instances
fork : duplicate the TS to another application
merge : merge with a TS coming from another application
  merge service references (PAT, CAT, etc.)

## Slide 19: Switching between multiple inputs
tsswitch command
same plugins as tsp
various switching strategies
remote control using UDP

## Slide 20: Input and output plugins
Input plugins
  Files: TS, M2TS, PCAP
  Network: multicast IP, HLS, HTTP, SRT, RIST
  Hardware: tuners (DVB, ATSC, ISDB), Dektec (ASI, demodulators)
  Application: fork, memory, craft, null
Output plugins
  Files: TS, M2TS
  Network: multicast IP, HLS, SRT, RIST
  Hardware: Dektec (ASI, modulators), HiDes (modulators)
  Application: fork, memory, drop, media player

## Slide 21: Packet processing plugins
TS transformations
  PID or packet filtering, PSI/SI transformation or injection, service extraction or modification, etc.
TS regulation
  time regulation, time shifting, scheduled recording, etc.
TS analysis and monitoring
  TS analysis, PSI/SI extraction, PID, bitrate monitoring, ECM or EMM monitoring, etc.
TS scrambling & descrambling
  DVB SimulCrypt support for ECM / EMM injection
Data injection of extraction
  SCTE 35, T2-MI, MPE, Teletext
Any other processing you wish to develop…
  75 packet processing plugins available (version 3.29)

## Slide 22: PSI/SI tables manipulation
binary, XML or JSON

## Slide 23: MPEG tables and sections
Extraction from TS, injection into TS
Data formats
  binary
    raw sections
  XML
    fully documented in user’s guide
    easy to manually edit or process in applications
  JSON
    through automated XML-to-JSON conversion
    easy to process in applications, especially in Python
All formats are uniformly used
  TS extraction, modification, injection
  file manipulation

## Slide 24: Sample XML file
<?xml version="1.0" encoding="UTF-8"?>
<tsduck>
<PAT version="8" transport_stream_id="0x0012" network_PID="0x0010">
<service service_id="0x0001" program_map_PID="0x1234"/>
<service service_id="0x0002" program_map_PID="0x0678"/>
</PAT>
<PMT version="4" service_id="0x0456" PCR_PID="0x1234">
<CA_descriptor CA_system_id="0x0777" CA_PID="0x0251"/>
<component elementary_PID="0x0567" stream_type="0x12">
<ISO_639_language_descriptor>
<language code="fre" audio_type="0x45"/>
<language code="deu" audio_type="0x78"/>
</ISO_639_language_descriptor>
</component>
</PMT>
</tsduck>

## Slide 25: Multiple ways to update tables in a TS
Specialized plugins with predefined options
  BAT, CAT, NIT, PAT, PMT, SDT
Manual XML handling
  Extract the table as an XML file
  Edit the file
  Reinject the file
Automated XML modification
  Using « XML patch files »
  Flexible XML templates to update tables on the fly
  Similar to XSLT in principle, but much simpler

## Slide 26: Extending TSDuck
C++ transport stream programming

## Slide 27: Extending TSDuck
TSDuck is extensible
  Source code provided
      git clone https://github.com/tsduck/tsduck.git
  Common API for Linux, Windows and macOS
    DVB tuners, Dektec and HiDes devices are not supported on macOS
  Programmer’s guide
    doxygen-generated, see https://tsduck.io/
You can modify it yourself !

## Slide 28: Why extending TSDuck?
Identify your needs
Try to find a solution using existing TSDuck plugins
  review utilities and plugins
Try to extend an existing utility or plugin
  add new options
  add features, don’t modify existing behavior
  remain upward compatible
Develop your own plugin
  it is quite simple, really
Send your code back using a pull request
  so that everyone can benefit from it

## Slide 29: Coding hints
Don’t write a plugin from scratch
  use an existing one as code base
  choose one which is technically similar
    input? output? PSI/SI transformation? packet filtering?
Implement simple & elementary features
  preserve TSDuck philosophy
    develop several elementary plugins if necessary
    not a single big plugin implementing several features
Read the « TSDuck coding guidelines » document
  a recommended reading, although not required
RTFM
(as usual)

## Slide 30: Proprietary extensions
Reason: manipulation of confidential data
  private PSI/SI signalization
  conditional access system implementation
Completely independent source code and binary packages
  additional plugins
  additional commands
  dynamically merging inside TSDuck proprietary implementations of tables, descriptors, CAS data structures, naming, etc.
Compatible with TSDuck BSD license
Sample code in source code tree
  sample/sample-extension

## Slide 31: Using the TSDuck library
to develop third-party applications in C++, Java or Python

## Slide 32: TSDuck library
All TSDuck common code is in one large library
  libtsduck.so / libtsduck.dylib / tsduck.dll
Contains generic and reusable C++ code
  basic operating system independent features
    system, multi-treading, synchronization, networking, cryptography, etc.
  MPEG/DVB features
    TS packets, PSI/SI tables, sections and descriptors, demultiplexing, packetization, encapsulation, DVB tuners, etc.
Can be used in your application
  even if not part of TSDuck

## Slide 33: Software architecture
C++ applications
  all TSDuck features
Java or Python applications
  high-level features only
  interactions using JSON or XML
  memory buffers for input/output
Custom plugins
  C++ only

## Slide 34: Programmer’s guide
Online, see https://tsduck.io/doxy/
  automatically updated every night
Tutorials
  building TSDuck and applications using its library
  developing TSDuck plugins and extensions
  C++ library tutorial
  Java and Python bindings
Reference
  all C++, Java and Python classes

## Slide 35: Thank you
Any question?